## Slide 1: F2 Project – S2C fpga v2.2
BenTsai
MTD Implement
2016/7/15

## Slide 2: OUTLINE
Environment
  HW
  SW
Compiler
  Flash 規劃
  U-Boot 修改
  Linux 修改
MTD Usage
  MTD Info
  MTD Erase
  MTD Copy
Booting
待解決問題

## Slide 3: Environment

## Slide 4: Environment
HW
  S2C fpga bit file v2.2 (P2S1521A_0624_V2.2_S2C.bit)
SW
  Git clone
    repo init -u git@10.63.246.9:CDB/manifests/Linaro-15.06/linux/f2-fpga.git
    repo sync
  U-boot
    Branch : FTK_F2_FPGA
    Commit id : b5d0410a93cf89e1b2f2ea75cf8bdc506fc26966
  Kernel
    Branch : FTK_F2_FPGA
    Commit id : 9ff2a741255919040f193d466bab0249ef924679
  Buildroot
    Branch : FTK_F2_FPGA
    Commit id : 2397f9c1124fc26b3761d30c52f82b7782d43a51
  Build
    Branch : develop
    Commit id : 2a648fff7c2fd4579c5e090b14316e0cec377491

## Slide 5: Compiler

## Slide 6: Flash 規劃 – 20160715
MTD0
  U-Boot
    0x00000000 ~ 0x00040000, 0x40000
  ENV
    0x00040000 ~ 0x00060000, 0x20000
MTD1
  uImage
    0x00060000 ~ 0x00560000, 0x500000
MTD2
  uInitrd(rootfs.jffs2)
    0x00560000 ~ 0x02d60000, 0x2800000
MTD3
  board.dtb
    0x02d60000 ~ 0x02d70000, 0x10000
MTD4
  data
    0x02d70000 ~
ENV
Linux
U-Boot
Buildroot
dts
data

## Slide 7: U-Boot - flash
Mx25u51245g default setting
  File : drivers/mtd/spi/macronix.c
  修改spi_flash_probe_macronixs內
  spi_flash_cmd_write_status(flash, 0x40);
  將0x00改為0x40，這是將Quad Enable設
  為1，確保4 I/O模式可以正常執行。
  4 I/O ↹ 2 I/O 注意事項
    SCU 0x31000328 數值0x10E ↹ 0x10D (SoC Spec.)
    QE設成1是4 I/O必要條件(flash Spec)
  目前bit file 版本，SCU 0x31000328
  初始值為0x10E(4 I/O)，之後可能會改為
  0x10D(2 I/O)。

## Slide 8: U-Boot – default setting
ENV Saving Address
  File : include/configs/f2-fpga.h
  依照flash規劃，設定ENV Offset
  CONFIG_ENV_OFFSET 0x60000 → 0x40000
TEXT Base
  File : include/configs/f2-fpga.h
  修改Text base

## Slide 9: Linux - SPI
Device Tree
  File : arch/arm/boot/dts/f2-fpga.dts
  確認Device Tree Spi 設定
  Spi Vs Spi-nor, 思考spi flash是否應該掛載在spi bus上, 還是另外撰寫spi-nor driver.
  此外，spi device name 設定上目前有瑕疵。

## Slide 10: Linux – MTD Device
Device
  File : arch/arm/mach-socle/board_F2_FPGA.c
  依flash規劃，修改spi_flash_part內的數值

## Slide 11: Linux – MTD Driver
Driver
  mm menuconfig
  Device Drivers --->
  <*> Memory Technology Device (MTD) support --->
    <*> SPI-NOR device support --->
  Device Drivers --->
  <*> Memory Technology Device (MTD) support --->
    Self-contained MTD device drivers --->

## Slide 12: Linux – SPI Driver
Driver
  mm menuconfig
  Device Drivers --->
  <*> SPI support --->

## Slide 13: MTD Usage

## Slide 14: MTD Usage
MTD info
  mtdinfo [mtd device]
  example : mtdinfo /dev/mtd2
  cat /proc/mtd
Erase
  flash_erase [mtd device] [start block] [erase block number]
  example : flash_erase /dev/mtd2 0 640
  640可以從mtdinfo得到
Copy to Mtd device
  flashcp [file] [mtd device]
  example : flashcp ~/uInitrd /dev/mtd2

## Slide 15: Booting

## Slide 16: Booting From Flash
依照Flash 的規劃，in u-boot
Copy file to DDR from flash
  uImage : mdma 0x50000000 0x10060000 0x50000
  uInitrd : mdma 0x51000000 0x10560000 0x2800000
  dtb : mdma 0x54000000 0x12D60000 0x10000
Switch SPI-Nor AHB to APB
  mw.l 0x0908004c 0x01
Bootm
  bootm 0x50000000 0x051000000 0x54000000

## Slide 17: 待解決問題

## Slide 18: 待解決問題
Booting時，須先執行Spi-Nor AHB/APB切換不合理，思考kernel driver的修正方式
目前台北使用的source code，在啟spi controller後，不可以開啟DMA controller，會造成資料傳輸的問題，應該是driver與IP匹配上有問題。
SPI-Nor IP 4 I/O ↹ 2 I/O 與 address 4byte mode ↹ 3byte mode需要注意。
Spi device node name 目前driver撰寫上有些瑕疵