## Slide 1: F2 Project – S2C fpga v2.2
BenTsai
RTC Implement
2016/7/18

## Slide 2: OUTLINE
Environment
  HW
  SW
Compiler
  U-Boot 修改
  Linux 修改
Usage
  U-Boot - date
  Linux - hwclock

## Slide 3: Environment

## Slide 4: Environment
HW
  S2C fpga bit file v2.2 (P2S1521A_0624_V2.2_S2C.bit)
  參考文件 : S2C_RTC_HW.pptx
SW
  Git clone
    repo init -u git@10.63.246.9:CDB/manifests/Linaro-15.06/linux/f2-fpga.git
    repo sync
  U-boot
    Branch : FTK_F2_FPGA
    Commit id : b5d0410a93cf89e1b2f2ea75cf8bdc506fc26966
  Kernel
    Branch : FTK_F2_FPGA
    Commit id : 9ff2a741255919040f193d466bab0249ef924679
  Buildroot
    Branch : FTK_F2_FPGA
    Commit id : 2397f9c1124fc26b3761d30c52f82b7782d43a51
  Build
    Branch : develop
    Commit id : 2a648fff7c2fd4579c5e090b14316e0cec377491

## Slide 5: Compiler

## Slide 6: U-Boot – I2C
I2C Implement
  File : include/configs/f2-fpga.h
  開啟Socle I2C

## Slide 7: U-Boot – Cmd Date
M41T62 Implement & Date Cmd
  File : include/configs/f2-fpga.h
  確認i2c開啟
  開啟date cmd & m41t62
    CONFIG_SYS_RTC_BUS_NUM 若沒設定，則default 為0，即I2C0控制RTC

## Slide 8: Linux – i2c Driver
Driver
  mm menuconfig
  Device Drivers --->
  I2C support --->
  I2C Hardware Bus support --->
  <*> SOCLE I2C Controller

## Slide 9: Linux – RTC Driver
Driver
  mm menuconfig
  Device Drivers --->
  <*> Real Time Clock --->
    <*> ST M41T62/65/M41T80/81/82/83/84/85/87 and compatible

## Slide 10: Linux – I2C
Device Tree
  File : arch/arm/boot/dts/f2-fpga.dts
  確認Device Tree spi/rtc module 設定
  可參考socle wiki : http://10.63.246.9/mediawiki/index.php/F2_Test_Plan_RTC

## Slide 11: Linux – m41t62 driver -1
Driver
  File : drivers/rtc/rtc-m41t80.c， 詳細程式碼請參閱wiki

## Slide 12: Linux – m41t62 driver - 2
Driver
  File : drivers/rtc/rtc-m41t80.c， 詳細程式碼請參閱wiki
  http://10.63.246.9/mediawiki/index.php/F2_Test_Plan_RTC

## Slide 13: Usage

## Slide 14: Usage – U-boot
U-Boot - date
  Date setting
  example : 2016/07/18 13:53
  cmd : date 0718135316
  Date show
  cmd : date

## Slide 15: Usage – linux
Linux - hwclock
  hwclcok
  Date show
  cmd : hwclock –r
  Date set
    date
    hwclcok -w